Experimental Computer for Schools

Example

This example adds two numbers by loading the store with the values and then using a ‘Keyboard Reset’ to enter an instruction that adds the contents of two locations in the store, putting the result in a third location.

With the ESC replica on:

Press ‘Normal reset’

Press ‘1’
Press ‘2’
Press ‘Load addr’

Press ‘4’
Press ‘5’
Press ‘point’
Press ‘3’
Press ‘Load store’

Press ‘Incr addr’

Press ‘1’
Press ‘3’
Press ‘point’
Press ‘9’
Press ‘Load store’

The two values to add are now in store locations 11 and 12.

Now, enter and run the addition instruction:

Press ‘Ki Reset’
Type the number: ‘70101112’

This is the instruction code.

Press ‘A’

The first stage of the instruction is processed (store addresses are shown)

Press ‘B’

The second stage of the instruction has been processed. The contents of the store locations are shown. These are the two values that will be added.

Press ‘C’
The instruction is processed to completion. The sum can be seen as the contents of store location 10:

Press ‘1’
Press ‘0’
Press ‘Load addr’