Experimental Computer for Schools Instruction Map

b	a->	0	1	2	3	4	5	6	7	8	9
0		(Rc)<-(Rc)+d	(Rc)<-(Rc)+(Rd)	Copy (Aa) into R0 and R1	Copy (Aa) into R0 and R1	Copy (Aa) into R0 and R1	Copy (Aa) into R0 and R1	Copy (Aa) into R0 and R1	(Aa1)<-(Aa2)+(Aa3)	(Aa1)<-(Aa2)+(Aa3)	(Aa1)<-(Aa2)+(Aa3)
1		(Rc)<-(Rc)-d	(Rc)<-(Rc)-(Rd)	Store R0 and R1 in Aa in data format	Store R0 and R1 in Aa in data format	Store R0 and R1 in Aa in data format	Store R0 and R1 in Aa in data format	Store R0 and R1 in Aa in data format	(Aa1)<-(Aa2)-(Aa3)	(Aa1)<-(Aa2)-(Aa3)	(Aa1)<-(Aa2)-(Aa3)
2		(Rc)<-d-(Rc)	(Rc)<-(Rd)-(Rc)	Store R0 and R1 in Aa in instruction format	Store R0 and R1 in Aa in instruction format	Store R0 and R1 in Aa in instruction format	Store R0 and R1 in Aa in instruction format	Store R0 and R1 in Aa in instruction format	(Aa1)<-(Aa2)*(Aa3)	(Aa1)<-(Aa2)*(Aa3)	(Aa1)<-(Aa2)*(Aa3)
3		(Rc)<-d	(Rc)<-(Rd)						(Aa1)<-(Aa2)/(Aa3)	(Aa1)<-(Aa2)/(Aa3)	(Aa1)<-(Aa2)/(Aa3)
4			Copy sign and RH size digits of Rd into Rc	Unconditional branch to Aa, Store link address in Rlink	Unconditional branch to Aa, Store link address in Rlink	Unconditional branch to Aa, Store link address in Rlink	Unconditional branch to Aa, Store link address in Rlink	Unconditional branch to Aa, Store link address in Rlink	Branch to Aa1 if (Aa2) = (Aa3)	Branch to Aa1 if (Aa2) = (Aa3)	Branch to Aa1 if (Aa2) = (Aa3)
5		Test (Rc)		Branch to Aa if CL=1 / Store links address in Rlink	Branch to Aa if CL=1 / Store links address in Rlink	Branch to Aa if CL=1 / Store links address in Rlink	Branch to Aa if CL=1 / Store links address in Rlink	Branch to Aa if CL=1 / Store links address in Rlink	Branch to Aa1 if (Aa2) > (Aa3)	Branch to Aa1 if (Aa2) > (Aa3)	Branch to Aa1 if (Aa2) > (Aa3)
6		Left Shift (Rc) by d places	Left Shift (Rc) by (Rd) places	Branch to Aa if CL=0 / Store links address in Rlink	Branch to Aa if CL=0 / Store links address in Rlink	Branch to Aa if CL=0 / Store links address in Rlink	Branch to Aa if CL=0 / Store links address in Rlink	Branch to Aa if CL=0 / Store links address in Rlink	Branch to Aa1 if |(Aa2)| > |(Aa3)|	Branch to Aa1 if |(Aa2)| > |(Aa3)|	Branch to Aa1 if |(Aa2)| > |(Aa3)|
7		Right Shift (Rc) by d places	Right Shift (Rc) by (Rd) places	Store Rlink in Aa	Store Rlink in Aa	Store Rlink in Aa	Store Rlink in Aa	Store Rlink in Aa	If (Aa1) <> 0 branch to (Aa2) and store Rlink in (Aa3)	If (Aa1) <> 0 branch to (Aa2) and store Rlink in (Aa3)	If (Aa1) <> 0 branch to (Aa2) and store Rlink in (Aa3)
8				Input Aa	Input Aa	Input Aa	Input Aa	Input Aa	Input (Aa1) and display (Aa1),(Aa2),(Aa3)	Input (Aa1) and display (Aa1),(Aa2),(Aa3)	Input (Aa1) and display (Aa1),(Aa2),(Aa3)
9			Stop and display Rc and Rd	Display Aa	Display Aa	Display Aa	Display Aa	Display Aa	Stop and display (Aa1), (Aa2), (Aa3)	Stop and display (Aa1), (Aa2), (Aa3)	Stop and display (Aa1), (Aa2), (Aa3)