# Schools Computer Assembly Language

The schools computer did not have an assembly language defined, instructions were entered and viewed as numeric values. To aid creation of programs on a PC that can then be sent to the simulation, an assembly language is defined here.

Mnemonic	Instruction Code
LD Rc, Rc + d	00cd
LD Rc, Rc – d	01cd
LD Rc, d – Rc	02cd
LD Rc, d	03cd
TEST Rc = 0	05c0
TEST Rc > 0	05c1
TEST Rc < 0	05c2
TESTLD Rc = 0	05c3
TESTRD Rc = 0	05c4
SL Rc, d	06cd
SR Rc, d	07cd
LD Rc, Rc + Rd	10cd
LD Rc, Rc – Rd	11cd
LD Rc, Rd – Rc	12cd
LD Rc, Rd	13cd
CPSR6 Rc, Rd	14cd
SL Rc, Rd	16cd
SR Rc, Rd	17cd
COPY R0, R1, cd	20cd
STORED R0, R1, cd	21cd
STOREI R0, R1, cd	22cd
BRL cd	25cd
BRL C0, cd	26cd
STL cd	27cd
IN cd	28cd
DISP cd	29cd
COPY R0, R1, (cd+R3)	30cd
STORED R0, R1, (cd+R3)	31cd
STOREI R0, R1, (cd+R3)	32cd
BRL cd+R3	35cd
BRL C0, cd+R3	36cd
STL (cd+R3)	37cd
IN (cd+R3)	38cd
DISP (cd+R3)	39cd
COPY R0, R1, (cd+R4)	40cd
STORED R0, R1, (cd+R4)	41cd
STOREI R0, R1, (cd+R4)	42cd
BRL cd+R4	45cd
BRL C0, cd+R4	46cd
STL (cd+R4)	47cd
IN (cd+R4)	48cd
DISP (cd+R4)	49cd
COPY R0, R1, (cd+R5)	50cd
STORED R0, R1, (cd+R5)	51cd
STOREI R0, R1, (cd+R5)	52cd
BRL cd+R5	55cd
BRL C0, cd+R5	56cd
STL (cd+R5)	57cd
IN (cd+R5)	58cd
DISP (cd+R5)	59cd
COPY R0, R1, (cd)	60cd
STORED R0, R1, (cd)	61cd
STOREI R0, R1, (cd)	62cd
BRL (cd)	65cd
BRL C0, (cd)	66cd
STL (cd)	67cd
IN (cd)	68cd
DISP (cd)	69cd