Experimental School’s Computer

Programs

This document is a collection of programs for the experimental school’s computer from around 1970. There are not very many programs known, these all come from the first course on the school’s computer.

A Program to Compute the Surface Area and Volume of a Sphere.

Address	Contents	Comments
0		Spare
1		Spare
2	r
3	a
4	b
5	3.14159
6	4
7	3
8		Spare
9		Spare
10	7802 0507	Input r; display 3.14159 and 3
11	7203 0202	a ← r x r
12	7203 0305	a ← a x 3.14159
13	7203 0306	a ← a x 4
14	7204 0302	b ← a x r
15	7304 0407	b ← b / 3
16	7902 0304	Display r, a and b
17
18
19
20